## Slide 1: ACA Final Project Memory Scheduler
王立 葉佳韋
葉丹 賴君濠

## Slide 2: Outline
Baseline
  First Come First Serve (FCFS)
Motivation
Mechanism
  Locality-Aware Scheduling
  Traffic Light
  Thread Categorizing
  Read Write Interleave
  Auto-Precharge

## Slide 3: Motivation
FCFS Issues
  Thread priority
    Thread behavior
    Blocked thread
  No row hit first
    Only consider requests’ coming time
  Read/Write Mode
    Read do read
    Write do write
  Close page policy
    Close if no row hit

## Slide 4: Locality-Aware
Main idea
  Exploit the maximum row buffer locality
When no any row hit requests
  Issue the request with the max row buffer hit count in read/ write queue
Row decoder
Row buffer
No any row buffer hit in queue
Issue the request with the max row buffer hit count
Queue

## Slide 5: Traffic light[4]
Main idea
  Some threads will be blocked because the demand channel is busy
    Refresh blocked thread
    Write drain mode blocked thread
Give the blocked thread lower priority

## Slide 6: Thread Categorizing[3]
Main idea
  Make cores as busy as possible
    Critical request first
Two Type
  Compute intensive thread - Higher priority
  Memory intensive thread - Lower priority
How to categorize
  Use two counters to trace
    Compute intensive counter
      Non-memory requests
    Memory intensive counter
      Memory requests
Time
Non-memory request
Memory request
Memory counter++
Compute counter++
Counter Over threshold
Compute intensive
Memory intensive
Reset

## Slide 7: Read Write Interleave[2]
Main idea
  Fully memory utilization
  Row hit first
Write Mode
  Write row hit first
  If no write row hit, read row hit first
  Otherwise, write FCFS
  Otherwise, read FCFS
Read Mode
  Read row hit first
  If no read row hit, write row hit first
  Otherwise, read FCFS
  Otherwise, write FCFS
... Delayed Close Page … How about read

## Slide 8: Auto-Precharge[5]
Main idea
  Adaptive close page policy
If the request has no row hit locality
  Auto-precharge after issuing the request

## Slide 9: Hardware Overhead
Assume 16 threads, Read queue size: 160 requests, Write queue size: 96 requests
Locality-Aware
  4KB is enough
Traffic Light
  16 bit = 2B
Thread Categorizing
  16 bit (thread phase status) = 2B
  16 x 4 = 64 bit (memory request frequency) = 8B
  16 x 10 = 160 bit (commit count) = 20B
Total: about 4KB space overhead

## Slide 10: Result
Workload | Config | Sum of exec times (10M cyc) |  |  |  |  |  | Max Slowdown |  |  |  |  | 
 |  | FCFS | A | B | C | D | E | FCFS | A | B | C | D | E
MT-canneal | 1 chan | 418 | 431 | 431 | 422 | 382 | 380 | N/A | N/A | N/A | N/A | N/A | N/A
MT-canneal | 4 chan | 179 | 174 | 173 | 173 | 176 | 163 | N/A | N/A | N/A | N/A | N/A | N/A
bl-bl-fr-fr | 1 chan | 149 | 150 | 150 | 150 | 143 | 143 | 1.2 | 1.21 | 1.21 | 1.21 | 1.14 | 1.15
bl-bl-fr-fr | 4 chan | 80 | 79 | 79 | 79 | 80 | 76 | 1.11 | 1.10 | 1.10 | 1.09 | 1.10 | 1.05
cl-cl | 1 chan | 83 | 83 | 84 | 84 | 82 | 82 | 1.12 | 1.12 | 1.12 | 1.12 | 1.10 | 1.10
cl-cl | 4 chan | 51 | 51 | 52 | 51 | 53 | 47 | 1.05 | 1.05 | 1.05 | 1.05 | 1.08 | 0.96
cl-cl-c2-c2 | 1 chan | 242 | 245 | 245 | 247 | 229 | 225 | 1.48 | 1.50 | 1.51 | 1.57 | 1.45 | 1.40
cl-cl-c2-c2 | 4 chan | 127 | 125 | 125 | 125 | 128 | 117 | 1.18 | 1.16 | 1.16 | 1.15 | 1.17 | 1.07
c2 | 1 chan | 44 | 44 | 44 | 44 | 44 | 44 | N/A | N/A | N/A | N/A | N/A | N/A
c2 | 4 chan | 30 | 30 | 30 | 30 | 31 | 28 | N/A | N/A | N/A | N/A | N/A | N/A
fa-fa-fe-fe | 1 chan | 228 | 232 | 232 | 228 | 210 | 209 | 1.52 | 1.55 | 1.56 | 1.51 | 1.39 | 1.39
fa-fa-fe-fe | 4 chan | 106 | 104 | 104 | 103 | 102 | 96 | 1.22 | 1.20 | 1.20 | 1.20 | 1.17 | 1.11
fl-fl-sw-sw-c2-c2-fe-fe | 4 chan | 295 | 294 | 293 | 293 | 275 | 264 | 1.4 | 1.38 | 1.38 | 1.40 | 1.32 | 1.25
fl-fl-sw-sw-c2-c2-fe-fe-bl-bl-fr-fr-c1-c1-st-st | 4 chan | 651 | 657 | 655 | 659 | 594 | 584 | 1.9 | 1.91 | 1.90 | 1.86 | 1.65 | 1.63
fl-sw-c2-c2 | 1 chan | 249 | 251 | 249 | 250 | 234 | 232 | 1.48 | 1.50 | 1.47 | 1.52 | 1.40 | 1.37
fl-sw-c2-c2 | 4 chan | 130 | 128 | 128 | 128 | 130 | 121 | 1.13 | 1.11 | 1.11 | 1.12 | 1.15 | 1.05
st-st-st-st | 1 chan | 162 | 162 | 164 | 163 | 154 | 152 | 1.28 | 1.28 | 1.29 | 1.28 | 1.21 | 1.21
st-st-st-st | 4 chan | 86 | 85 | 84 | 84 | 85 | 81 | 1.14 | 1.13 | 1.13 | 1.12 | 1.14 | 1.07
Overall |  | 3312 | 3325 | 3321 | 3313 | 3130 | 3043 | 1.3 | 1.3 | 1.3 | 1.3 | 1.25 | 1.2
 | Percentage |  | -0.39% | -0.27% | -0.03% | 6.4% | 8.2% | PFP:3438 | PFP:3441 | PFP:3435 | PFP:3437 | PFP:3438 | PFP:2918
A: LocalityAware
B: A + TrafficLight
C: B + Thread Categorizing
D: C + RW Interleave
E: D + Auto Precharge
1 channel degrades
Reason:
Too aggressive, less active threads
No channel level parallelism

## Slide 11: Reference
Parallelism-Aware Batch Scheduling: Enhancing both Performance and Fairness of Shared DRAM Systems - Onur Mutlu, Thomas Moscibroda
The Compact Memory Scheduling Maximizing Row Buffer Locality , Young-Suk Moon, Yongkee Kwon, Hong-Sik Kim, Dong-gun Kim, Hyungdong Hayden Lee, and Kunwoo park (SK Hynix).
High Performance Memory Access Scheduling using Compute-Phase Prediction and Writeback-Refresh Overlap , Yasuo Ishii (The University of Tokyo, NEC Corporation) and Kouhei Hosokawa, Mary Inaba, and Kei Hiraki (The University of Tokyo).
Service Value Aware Memory Scheduler by Estimating Request Weight and Using per-Thread Traffic Lights , Keisuke Kuroyanagi (INRIA/IRISA, The University of Tokyo) and Andre Seznec (INRIA/IRISA).
Introduction to the USIMM Simulation Infrastructure for the Memory Scheduling Championship , Niladrish Chatterjee (University of Utah).